## Slide 1: Compilers
Lecture-1

## Slide 2: Today’s topics
Introduction to Compilers
Programming languages
X86_64 assembly
Interpreters
Memory safety

## Slide 3: Course Webpage
Google classroom: xbdx6em

## Slide 4: Books
Compiler Principles, Techniques and Tools (Second Edition)
  Alfred Aho, Monica Lam, Ravi Sethi and Jeffrey Ullman
Engineering a Compiler (Second Edition)
  Keith Cooper and Linda Torczon

## Slide 5: Tentative plan
X86 instruction set
LLVM IR
Local and global optimizations
Data flow analysis
Static single-assignment
Register allocation
Type checking
Memory safety
Garbage collection
Scanners
Regular expressions
NFA, DFA
Parsers
Context free grammars
Type inference
Code generation

## Slide 6: Grading components
Mid-term: 25
End-term: 30
Assignments (individual + group): 35
Homeworks (handwritten, in-class submission): 10
Bonus (class participation, in-class exercises, etc.): 20
Final marks in the assignments = min(actual marks + bonus, 35)

## Slide 7: Homework
The hand-written homework submission will only be accepted in the class at the start of the lecture
  Sharing your homework sheet with anybody else will be counted as plagiarism
  To submit homework, you need to attend the lecture
You are not allowed to enter the classroom after 9:35 AM on Wednesday and 11:05 AM on Friday

## Slide 8: Assignments
Any installation-related query should be initiated within the first five days after the assignment is released
You can send your queries over email or discuss them after the class

## Slide 9: Office hours
Wednesday: 10:30 AM – 11:00 AM
Friday: Noon – 12:30 PM
If you want to meet me during office hours, inform me just after the lecture

## Slide 10: TA
Gopi Krishna Menon
Office hours: Monday, Noon - 1:00 PM, A-518, R&D block

## Slide 11: Prerequisite
Strong C/C++ skills

## Slide 12: Postconditions
Can design new optimizations
Get hands-on experience with
  Optimizations
    Assignment on implementing data-flow analysis in LLVM
  runtime systems
    Assignment on implementing GC
  front end
    Homework on the generating front end for a given grammar
  type checking/ code generation
    Assignment on type and spatial safety in C using runtime instrumentation

## Slide 13: What is Compiler?
A Compiler is a tool that converts a program developed in one language to another language
  Compiler doesn’t change the meaning of a program

## Slide 14: Programming languages
Why do we have so many programming languages?

## Slide 15: Why do we need different languages?
A programming language reduces the programmers’ effort in application development
  e.g., SQL language is used for developing database applications
SELECT * FROM Customers WHERE City IN (‘New Delhi’);
The above statement prints all the records from a table named Customers where the customer’s city is New Delhi

## Slide 16: Why do we need different languages?
SQL query:
SELECT * FROM Customers WHERE City IN (‘New Delhi’);
The equivalent C code is much more complicated.
In other words, the SQL language reduces programmers’ effort to develop database applications.

## Slide 17: Why do we need different languages?
Similarly, there are languages other than SQL that target a different domain called domain-specific languages
  e.g., HTML for web pages, P4 for network devices, etc.
Other than domain-specific languages, we also have general-purpose languages
  e.g., C, C++, Java, Rust, etc.

## Slide 18: Programming languages
Why do we have multiple general-purpose languages
  e.g., C, C++, Java, Rust, etc.

## Slide 19: Advantages of using Java over C++

## Slide 20: Advantages of using Java over C++
Java is a safe language
  Memory safety
    Temporal safety: no use-after-free
    Spatial safety: no out-of-bounds array accesses
  Type safety
    No arbitrary typecasts

## Slide 21: Programming assignments
In the programming assignments, we will try to extend the C language to provide memory safety

## Slide 22: Compilers

## Slide 23: What is Compiler?
A Compiler is a tool that converts a program developed in one language to another language
  Compiler doesn’t change the meaning of a program

## Slide 24: Compiler for C
Assuming all applications are C applications
  Do we need a compiler for C?

## Slide 25: Compiler for C
Assuming all applications are C applications
  Do we need a compiler for C?
    Yes, because CPU doesn’t understand the C language
    After all, our application is going to execute on CPU
    We need to convert C programs into the CPU’s language in order to execute them

## Slide 26: What is the language of a CPU?
CPU language consists of instructions provided by the CPU architects
Different architectures have different sets of instructions
  ARM, X86, PowerPC, etc. have different instructions sets
An instruction is a sequence of byte-code
  0x89, 0x01, 0xc3

## Slide 27: Data storage
In the linked-list program from your data-structure course, at which hardware component the linked-list nodes are stored

## Slide 28: Data storage
In the linked-list program from your data-structure course, at which hardware component the linked-list nodes are stored
  The linked-list nodes are stored in the RAM

## Slide 29: X86_64 CPU
16 registers (64-bit)
  RAX, RCX, RDX, RBX, RSI, RDI, RBP, RSP, R8, R9, R10, R11, R12, R13, R14, R15
Memory
  RAM/ROM/Devices
  264 unique addresses
    Writing to memory means writing to a memory address
    Reading from memory means reading from a memory address
0
264-1
Notes: The program variables and data stored in different data structures, such as arrays, linked lists, trees, etc., are stored in a register or memory.

## Slide 30: X86_64 Register
0
15
31
63
EAX
RAX
 | AH | AL
AX
7
Read section-3.4.1 from the Intel manual-1.

## Slide 31: X86_64 Register
0
15
31
63
EBX
RBX
 | BH | BL
BX
7

## Slide 32: X86_64 Register
0
15
31
63
ECX
RCX
 | CH | CL
CX
7

## Slide 33: X86_64 Register
0
15
31
63
EDX
RDX
 | DH | DL
DX
7

## Slide 34: X86_64 Registers
0-7 | 8-15 | 0-15 | 0-31 | 0-63
AL | AH | AX | EAX | RAX
BL | BH | BX | EBX | RBX
CL | CH | CX | ECX | RCX
DL | DH | DX | EDX | RDX
DIL | - | DI | EDI | RDI
SIL | - | SI | ESI | RSI
BPL | - | BP | EBP | RBP
SPL | - | SP | ESP | RSP
R8L – R15L | - | R8W – R15W | R8D – R15D | R8 – R15

## Slide 35: Example
int main() {
unsigned long long v1;
unsigned long long *p1 = malloc(8);
unsigned *p2 = malloc(4);
unsigned v2;
*p1 = 100;
*p2 = 20;
v1 = *p1;
v2 = *p2;
v1 += 20;
…
}
Data can be stored in registers or memory.
Notes: In this example, the values of v1, p1, p2, v2 can be stored in different registers, e.g., RAX, RBX, RCX, EDX, respectively. malloc returns an address of the RAM. When we do *p1 = 100, 8-byte 100 is stored in the RAM address stored in p1 (or RBX). When we do v2 = *p2, the 4-byte value stored at the address stored in p2 (or RCX) is read into v2 (or EDX). When we do v1 += 20, 20 is added to RAX, and the result is stored in the RAX.

## Slide 36: X86_64 CPU
Different kinds of instructions
  Moving a constant to a register
  Moving data from a register to a register
  Moving data from memory to a register (memory-read/ load)
  Moving data from a register to memory (memory-write/ store)
  Performing an arithmetic operation on registers
  Performing an arithmetic operation on a register and memory
  Memory/memory operations are rare (string instructions)
int main() {
unsigned long long v1, v2;
unsigned long long *p1, *p2;
p1 = malloc(8);
p2 = malloc(8);
v1 = 10;
v1 = v2;
*p1 = v1;
*p2 = v2;
v1 = *p1;
v2 = *p2;
v1 += v2;
(*p1) += v1;
*p1 = *p2;
}

## Slide 37: X86_64 CPU
Different kinds of instructions
  Moving a constant to a register
    Line-6
  Moving data from a register to a register
    Line-7
  Moving data from memory to a register (memory-read/ load)
    Line-10 and 11
  Moving data from a register to memory (memory-write/ store)
    Line-8 and 9
  Performing an arithmetic operation on registers
    Line-12
  Performing an arithmetic operation on a register and memory
    Line-13
  Memory/memory operations are rare (string instructions)
    Line-14
int main() {
unsigned long long v1, v2;
unsigned long long *p1, *p2;
p1 = malloc(8);
p2 = malloc(8);
v1 = 10;
v1 = v2;
*p1 = v1;
*p2 = v2;
v1 = *p1;
v2 = *p2;
v1 += v2;
(*p1) += v1;
*p1 = *p2;
}

## Slide 38: X86_64 instructions
.byte 0x48 0x89 0x08
CPU instructions are byte-code.
It is hard to write computer programs using byte-code.

## Slide 39: Assembly language
An assembly language allows programmers to write CPU instructions in a user-friendly format
An assembler can be used to convert an assembly program into the CPU byte-code.

## Slide 40: Assembly language
.byte 0x48 0x89 0x08 mov %rcx, (%rax)
Store the 64-bit value in the rcx register into the memory address stored in the rax register

## Slide 41: Assembly language
Instruction | C equivalent | 
mov $10, %rax |  | storing constant in a register
mov %rcx, %rax |  | register to register
mov %rcx, (%rax) |  | store
mov (%rax), %rcx |  | load
mov 0x1000, %rax |  | load
add %rax, %rcx |  | register arithmetic
add $100, %rax |  | register and constant
sub %rax, %rcx |  | register arithmetic
sub $100, %rax |  | register and constant
call foo |  | 
ret |  | 
jmp label |  | 
Notes: This slide lists some x86 instructions and their C equivalent.

## Slide 42: Assembly language
Instruction | C equivalent | 
mov $10, %rax | rax = 10 | storing constant in a register
mov %rcx, %rax | rax = rcx | register to register
mov %rcx, (%rax) | *((unsigned long long*)rax) = rcx; | store
mov (%rax), %rcx | rcx = *((unsigned long long*)rax); | load
mov 0x1000, %rax | rax = *((unsigned long long*)0x1000); | load
add %rax, %rcx | rcx = rcx + rax; | register arithmetic
add $100, %rax | rax = rax + 100; | register and constant
sub %rax, %rcx | rcx = rcx – rax; | register arithmetic
sub $100, %rax | rax = rax – 100; | register and constant
call foo | foo(); | 
ret | return; | 
jmp label | goto label; | 
Notes: This slide lists some x86 instructions and their C equivalent. The type of rax and rcx is unsigned long long in the equivalent C code.

## Slide 43: Assembly language
If hardware understands assembly language, why can’t we implement everything using assembly language
  Why do we need a compiler?

## Slide 44: Assembly language
If hardware understands assembly language, why can’t we implement everything using assembly language
  Why do we need a compiler?
    Writing computer programs using assembly language is hard
    Computer languages (C, Java, SQL, etc.) reduce the complexity in software development and thus improves programmers’ productivity

## Slide 45: Why writing software in assembly is hard?
100 + 200
Instruction | C equivalent
mov $10, %rax | rax = 10
mov %rcx, %rax | rax = rcx
mov %rcx, (%rax) | *((unsigned long long*)rax) = rcx;
mov (%rax), %rcx | rcx = *((unsigned long long*)rax);
mov 0x1000, %rax | rax = *((unsigned long long*)0x1000);
add %rax, %rcx | rcx = rcx + rax;
add $100, %rax | rax = rax + 100;
sub %rax, %rcx | rcx = rcx – rax;
sub $100, %rax | rax = rax – 100;
call foo | foo();
ret | return;
jmp label | goto label;

## Slide 46: Why writing software in assembly is hard?
100 + 200
mov $100, %rax
mov $200, %rcx
add %rax, %rcx
Instruction | C equivalent
mov $10, %rax | rax = 10
mov %rcx, %rax | rax = rcx
mov %rcx, (%rax) | *((unsigned long long*)rax) = rcx;
mov (%rax), %rcx | rcx = *((unsigned long long*)rax);
mov 0x1000, %rax | rax = *((unsigned long long*)0x1000);
add %rax, %rcx | rcx = rcx + rax;
add $100, %rax | rax = rax + 100;
sub %rax, %rcx | rcx = rcx – rax;
sub $100, %rax | rax = rax – 100;
call foo | foo();
ret | return;
jmp label | goto label;
Notes: This slide shows a simple assembly program that adds two numbers and stores their sum in the rcx register.

## Slide 47: Why writing software in assembly is hard?
Take 10 inputs (64-bit) from user and compute their sum
// takes 10 inputs from user in input buffer
// readuser_asm (unsigned long long *buf);
1. mov $0x1000, %rax
2. call readuser_asm
3. mov $0, %rdx
4. mov $0x1000, %rax
5. mov (%rax), %rcx
6. add %rcx, %rdx // rdx = buf[0]
7. mov $1008, %rax
8. mov (%rax), %rcx
9. add %rcx, %rdx // rdx = buf[0] + buf[1]
..
Instruction | C equivalent
mov $10, %rax | rax = 10
mov %rcx, %rax | rax = rcx
mov %rcx, (%rax) | *((unsigned long long*)rax) = rcx;
mov (%rax), %rcx | rcx = *((unsigned long long*)rax);
mov 0x1000, %rax | rax = *((unsigned long long*)0x1000);
add %rax, %rcx | rcx = rcx + rax;
add $100, %rax | rax = rax + 100;
sub %rax, %rcx | rcx = rcx – rax;
sub $100, %rax | rax = rax – 100;
call foo | foo();
ret | return;
jmp label | goto label;
Notes: In this program, the readuser_asm routine takes a buffer of size 80 bytes in the rax register and reads ten inputs (of size 8 bytes) from the user into the buffer. The assembly code allocates a RAM buffer at address 0x1000 of size 80 bytes. The address of the buffer is passed to the readuser_asm in the register rax (at line-1). After returning from readuser_asm, at line-3, the program initializes the rdx register to zero (line-3) and sets the rax register to the address of buf[0] (line-4). At line-5, the value of buf[0] is read in the rcx register. At line-6, the contents of buf[0] are added to the rdx register, and the result is stored in rdx. At this point, the rdx register contains the value of buf[0]. At line-7, rax is set to the address of buf[1]. At line-8, the value of buf[1] is read in the rcx register. At line-9, we compute the sum of rdx and buf[1] and store it to rdx. At this point, rdx contains buf[0] + buf[1]. We need to repeat this process until the rdx register contains the sum of all ten elements.

## Slide 48: Why writing software in assembly is hard?
Take 10 inputs (64-bit) from user and sort them
// takes 10 inputs from user in input buffer
// readuser_asm (unsigned long long *buf);
Instruction | C equivalent
mov $10, %rax | rax = 10
mov %rcx, %rax | rax = rcx
mov %rcx, (%rax) | *((unsigned long long*)rax) = rcx;
mov (%rax), %rcx | rcx = *((unsigned long long*)rax);
mov 0x1000, %rax | rax = *((unsigned long long*)0x1000);
add %rax, %rcx | rcx = rcx + rax;
add $100, %rax | rax = rax + 100;
sub %rax, %rcx | rcx = rcx – rax;
sub $100, %rax | rax = rax – 100;
call foo | foo();
ret | return;
jmp label | goto label;
Notes: In this exercise, we would like to sort the buffer after taking input from the user. As you might have imagined, this is going to be much more complicated. If you are not convinced, please go ahead and try.

## Slide 49: Why writing software in assembly is hard?
// Create a linked list
struct Node {
int Val;
struct Node *Next;
};
// No types in an assembly language
// Even if somebody manages to write a correct program, it would be hard for a third person to make sense of the given program
// Managing and debugging would be extremely hard
// One may need to put a lot of effort to implement even an elementary program like a linked list in an assembly language
Instruction | C equivalent
mov $10, %rax | rax = 10
mov %rcx, %rax | rax = rcx
mov %rcx, (%rax) | *((unsigned long long*)rax) = rcx;
mov (%rax), %rcx | rcx = *((unsigned long long*)rax);
mov 0x1000, %rax | rax = *((unsigned long long*)0x1000);
add %rax, %rcx | rcx = rcx + rax;
add $100, %rax | rax = rax + 100;
sub %rax, %rcx | rcx = rcx – rax;
sub $100, %rax | rax = rax – 100;
call foo | foo();
ret | return;
jmp label | goto label;
Notes: Developing and managing large software without types is very much challenging.

## Slide 50: Portability
Different architectures have different instruction sets
The same program can be compiled for different architectures
One need to rewrite the whole application to support a different architecture if the application was primarily developed in an assembly language

## Slide 51: Summary
Compiler is needed
  To convert a program from a source language to a target language
    Commonly used target language is an assembly language
  To generate byte-codes for different architectures for a given program

## Slide 52: Language for compiler development
Can we develop a compiler for the C language in C itself?

## Slide 53: Language for compiler development
Can we develop a compiler for the C language in C itself?
  The first compiler needs to be developed in either assembly or a language for which a compiler already exists
  Once we have a working compiler for C (say Alpha) then we can write a compiler for C in the C language itself (say Beta)
  Beta can be compiled using Alpha
  Once we have a compiled Beta compiler we can compile future versions of Beta using previous versions of Beta

## Slide 54: Advantage of using compilers
Architectures have limited number of registers
Register accesses are faster than memory accesses
A program can use a lot of variables at a given time
  Variables can live in memory or registers
Compilers are good at register allocation
In general, compilers are good at optimizations

## Slide 55: Compiler optimizations
Compiler optimizations don’t change the meaning of the program
The goal of the compiler optimizations may vary depending on the use case
  Possible goals could be
    Reduce the total execution time of the application
    Reduce the latency
    Improve the throughput
    Reduce the size of the binary
    Reduce memory consumption, etc.

## Slide 56: Compiler optimizations
void foo (int **arr, int m, int n)
{
int i, j;
for (i = 0; i < m; i++) {
for (j = 0; j < n; j++) {
arr[i][j] = (i * 100) + j;
}
}
}
Our goal is to reduce the total execution time.

## Slide 57: Compiler optimizations
void foo (int **arr, int m, int n)
{
int i, j;
for (i = 0; i < m; i++) {
for (j = 0; j < n; j++) {
arr[i][j] = (i * 100) + j;
}
}
}
void foo (int **arr, int m, int n)
{
int i, j;
for (i = 0; i < m; i++) {
int tmp = i * 100;
for (j = 0; j < n; j++) {
arr[i][j] = tmp + j;
}
}
}
Notes: The (i*100) computation needs to be done only once outside the inner loop. Compilers can automatically infer and perform this optimization.

## Slide 58: Related tool
Interpreters

## Slide 59: Compiler
Compiler
main.c
a.out
a.out
input
output
Offline or Static
Runtime or Dynamic

## Slide 60: Interpreter
Interpreter
source
input
output
Runtime or Dynamic

## Slide 61: Interpreter
Interpreters transform the code during the execution of the program
  examples: Python, Perl, etc.
Advantage:
  Only transform the code that is actually going to run
  Good for prototyping
Disadvantage:
  Not efficient, runtime errors

## Slide 62: Interpreter
int search(int *arr, int n, int val) {
if (arr == NULL) {
printf(“error\n”)
exit(;
}
int i;
for (i = 0; i < n; i++) {
if (arr[i] == val) { return i; }
}
return -1;
}
Notes: Let us consider this program is being interpreted. In this mode, if the condition arr == NULL is never true, the interpreter will not generate code for printf and exit. Even if there is a syntax error in the if body, the users can successfully run this program because the interpreter never checks for error in the code that doesn’t execute at runtime. On the other hand, if you are using a compiler, all the code needs to be syntactically correct at compile time because the compiler assumes that all program paths are possible at runtime.

## Slide 63: Java
Instead of interpreting the actual program, the program is compiled into Java byte-code
  The Java-interpreter interprets the byte-code at runtime
COMPILER
INTERPRETER
JAVA PROGRAM
BYTE CODE
RESULTS
INPUT

## Slide 64: Java
Java also has a profiling phase that aims to minimize branch mispredictions and cache misses
  A significant optimization during the `90s
After a byte-code instruction is translated into the target assembly during the first execution, the translated code is cached and reused during future executions, and thus, the amortized cost of the translation is not high because, usually, the same piece of code executes a large number of times, e.g., a loop or function body

## Slide 65: Summary
Compilers are offline
  No code transformation at runtime
  Faster
  Generate syntax errors if any part of the code is syntactically incorrect
  Good for software in production
Interpreters are online
  Code transformation at runtime
  Slower
  Generate syntax errors for the parts of code that actually execute
  Good for prototyping