## Slide 2: Programming assignments
Five must submit programming assignments (20 Marks)
  We expect all of you to do these assignments
  Questions from assignments in the midsem and endsem
  do them to perform well in exams
Four optional assignments (16 Points)
  Optional assignments have prerequisites
  Demos for optional assignments will be conducted after the endsem
  You can do them to boost your marks or improve your learning, whichever suits you better
We will consider the min(20, must+optional+2) marks in the final grading

## Slide 3: Homework
min(10, marks obtained in homework) will be considered for final grading
Questions form homework in midsem and endsem
  do them perform well in exams

## Slide 4: How to learn OS
Do the programming assignments and homework
If you are struggling with C
  take help from the TAs and your friends who know C
  If you think you need a full semester course for C language, you can talk to HoD or other administrative people
Good knowledge of the C language is a prerequisite for the OS course

## Slide 5: Homework-2
int foo () {
int a, b, c, d, e, f;
a = 0, b = 1, c = 2, d = 3;
e = 5, f = 6;
bar(b, c, d, f);
return a + b + c;
}
foo: a(%eax), b(%ebx), c(%ecx), d(%edx), e(%esi), f(%edi)

## Slide 6: Homework-2
int bar(int a, int b, int c, int d) {
int x, y, z, w;
x = a, y = b, z = c, w = d;
return x + y + z + w;
}
bar: x(%eax), y(%ebx), z(%ecx), w(%edx)

## Slide 7: Homework-2
void foo (int a, int b) {
bar(&a, &b);
}

## Slide 8: Homework-2
int bar(int *x, int *y) {
*x = 0;*y = 1;
}

## Slide 9: Homework-2
int bar(int x, int y);
int foo (int a, int b) {
return bar(a, b);
}
00000000 <foo>:
0: 55 push %ebp
1: 89 e5 mov %esp,%ebp
3: 53 push %ebx
4: 83 ec 04 sub $0x4,%esp
7: e8 fc ff ff ff call 8 <foo+0x8>
c: 05 01 00 00 00 add $0x1,%eax
11: 83 ec 08 sub $0x8,%esp
14: ff 75 0c pushl 0xc(%ebp)
17: ff 75 08 pushl 0x8(%ebp)
1a: 89 c3 mov %eax,%ebx
1c: e8 fc ff ff ff call 1d <foo+0x1d> # bar
21: 83 c4 10 add $0x10,%esp
24: 8b 5d fc mov -0x4(%ebp),%ebx
27: c9 leave
28: c3 ret

## Slide 10: Homework-2
int x;
void foo() {
x = 0;
}

## Slide 11: Homework-2
foo(1, 4)
foo(1, 0, 6)
foo(2, 5, 9, 0)

## Slide 12: Homework-3
int schedule_disabled = 0; // global
struct list *ready_list; // global
struct thread *cur_thread; // global
void schedule1 () {
if (schedule_disabled) {
return;
}
schedule_disabled = 1;
push_list(ready_list, cur_thread);
schedule();
schedule_disabled = 0;
}

## Slide 13: Homework-3
Emulation of interrupt disable
int interrupt_disabled = 0;
In every interrupt handler:
cmp $0, interrupt_disabled
je 1f
iret
1: // original interrupt code

## Slide 14: Homework-3
bar:
push %ebp
mov %esp, %ebp
mov $100, %eax
mov %ebp, %esp
pop %ebp
ret
foo:
push %ebp
mov %esp, %ebp
mov $101, %eax
mov %ebp, %esp
pop %ebp
ret
interrupt_handler:
push %eax
push %edx
push %ecx
call schedule1
pop %ecx
pop %edx
pop %eax
iret
foo was preempted before.
bar is the current thread.

## Slide 15: context_switch(struct thread *prev, struct thread *next)
push %ebp
push %esi
push %edi
push %ebx
mov 20(%esp), %eax
mov %esp, (%eax) // prev->esp = %esp
mov 24(%esp), %eax
mov (%eax), %esp // %esp = next->esp
pop %ebx
pop %edi
pop %esi
pop %ebp
ret
struct thread {
void *esp;
};

## Slide 16: How to say hello to a device?

## Slide 17: Port I/O
Use dedicated I/O space
  Only 1024 I/O address
    also called ports
  accessed using in/out instructions
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
Notes: Apart from the physical address space, the hardware has a dedicated I/O space. The size of I/O space is very small (only 1024 addresses). These addresses are called ports. These ports are connected to devices. Software can talk to devices by reading/writing from/to these ports. Reading and writing to these ports are done through special instructions “in” and “out”. “in” instructions takes the address of the port as an argument and reads a (1,2,4) byte value from the port in the EAX register. Similarly, out instruction writes the value of the EAX register to a given port.

## Slide 18: Port I/O
Each device comes with a manual
  The manual talks about how to communicate with the device
  e.g., a printer device manual says, “if you want to say hello, please write 1 to port 100.”
  outl $100 instruction writes the content of the eax register to port 100
Notes: To write the four-byte one to port 100, the x86 CPU needs to execute “mov $1, %eax” and “outl $100” in that order.

## Slide 19: Port I/O
Each device comes with a manual
  On the next page, the manual says, “if you want to check if I have received your message, please read my status from port 101. I will set it to 1 after receiving your message.”
  inl $101 instruction reads a 4-byte value from port 101 in the register eax
Notes: The instruction “inl $101” reads a 4-byte value from port 101 into register %eax.

## Slide 20: Line printer (Port I/O)
#define DATA_PORT 0x378
#define STATUS_PORT 0x379
#define BUSY 0x80
#define CONTROL_PORT 0x37A
#define STROBE 0x01
void lpt_putc(int c) {
while((inb(STATUS_PORT) & BUSY) == 0) ; /* wait for printer to consume previous byte */
outb(DATA_PORT, ‘c’); /* put the byte on the parallel lines */
outb(CONTROL_PORT, STROBE); /* tell the printer to look at the data */
outb(CONTROL_PORT, 0);
}
Notes: inb routine reads a one-byte value from an input port (using in instruction). outb routine writes a one-byte value to a given port (using out instruction). This particular device requires OS to write 1 followed by 0 to the CONTROL_PORT after putting the data on the DATA_PORT.

## Slide 21: Memory mapped I/O
Some addresses in the physical address space are reserved for devices
Software talks to the devices by reading/writing to these addresses
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY
Notes: Apart from the port I/O, the devices can talk to CPU through memory-mapped I/O. Some part of the physical address space is reserved for devices (marked as MEMORY MAPPED DEVICES in this diagram). Software can talk to devices by reading/writing to these addresses.

## Slide 22: Memory mapped I/O
Each device comes with a manual
  The manual talks how to communicate with the device
  e.g., a printer device manual says, “if you want to say hello, please write 1 to address 0x100100.”
Notes: To access memory-mapped devices, we don’t need special instructions. We can do it in the C language itself.

## Slide 23: Memory mapped I/O
Each device comes with a manual
  On the next page, the manual says, “if you want to check if I have received your message, please read my status from address 0x100108. I will set it to 1 after receiving your message.”

## Slide 24: Line printer (MMIO)
volatile int *DATA_REG = 0xffffff00;
volatile int *STATUS_REG = 0xffffff04;
volatile int* CONTROL_REG = 0xffffff0C;
#define BUSY 0x80
#define STROBE 0x01
void lpt_putc(int c) {
while ((STATUS_REG[0] & BUSY) == 0) ; /* wait for printer to consume previous byte */
DATA_REG[0] = ‘c’; /* put the byte on the parallel lines */
CONTROL_REG[0] = STROBE; /* tell the printer to look at the data */
CONTROL_REG[0] = 0;
}
Notes: This is the same device code that we discussed before, but this time it is using MMIO.

## Slide 25: Compiler optimizations
We know that the compiler can use registers to save temporary computations
This results into further optimizations
  e.g., int *STATUS_REG = 0xffffff04; while ((STATUS_REG[0] & BUSY) == 0);
  can be rewritten to
    %eax = STATUS[0] & BUSY; while (%eax == 0);
  eliminating the load in a busy loop
  which results into an infinite loop

## Slide 26: Compiler optimizations
int *STATUS_REG = 0xffffff04;
while ((STATUS_REG[0] & BUSY) == 0);
%eax = STATUS[0] & BUSY;
while (%eax == 0); // infinite loop
Notes: The compiler can save temporary computations in registers to save loads/stores. This may result into an infinite loop.

## Slide 27: What went wrong?
This program works perfectly if compiler always loads the value in the loop
The compiler does not know that a device can change the value in the memory location
How to prevent the compiler from doing this optimization

## Slide 28: Optimization barrier
asm volatile (“”::: “memory”) prevents the compiler from performing this optimization.
  Read A.3.5 Optimization Barriers
    https://faculty.iiitd.ac.in/~piyus/pintos/doc/pintos_6.html#SEC98
All the values, which are cached in registers, are reloaded across the optimization barrier.

## Slide 29: Correct code
while ((STATUS_REG[0] & BUSY) == 0) {
asm volatile(“” ::: “memory”);
}

## Slide 30: volatile
the volatile keyword can also be used to prevent the compiler from caching the value of a variable in a register
volatile int *STATUS_REG = 0xffffff04;
while ((STATUS_REG[0] & BUSY) == 0) ;
Here, volatile makes sure that the value of the memory location will be loaded inside the loop.

## Slide 31: acquire
acquire(struct lock *l) {
status = interrupt_disable();
while (l->value == 0) {
list_push(l->wait_list, cur_thread);
schedule();
}
l->value = 0;
set_interrupt_status(status);
}
struct lock {
int value;
};
Is it possible that the compiler can transform this while loop into an infinite loop by loading the “l->value” in a register outside the loop?
No, because the compiler doesn’t know for sure that “l->value” can’t be modified in the “list_push” or “schedule” routines.

## Slide 32: Direct memory access (DMA)
Similar to CPU(s), devices can also directly access the RAM
  e.g., a network device can directly copy a packet from RAM to device memory and vice versa
  the device manual says how to configure the device to write an incoming packet to RAM or read a packet that needs to be sent from RAM
    the device needs to know the RAM addresses
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
UNUSED
EXTENDED MEMORY

## Slide 33: Send
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
Firefox puts the packet is at location x in the RAM.
CPU configures (using MMIO) NIC to start a DMA from location x.
CPU puts Firefox to a waiting list and starts executing other threads.
Notes: NIC: network interface card. NIC has its internal memory. During send, the packet needs to be copied from RAM to NIC’s internal memory.

## Slide 34: Send
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
CPU is executing other threads.
NIC is copying packet from memory location x to its internal buffer.
Both things are happening in parallel.

## Slide 35: Interrupt mode
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
NIC has copied the packet to its internal buffer. NIC sends interrupt to CPU.

## Slide 36: Interrupt mode
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
The interrupt handler is called. CPU sets the packet’s status to sent, puts Firefox to the ready list, and goes back to user mode.

## Slide 37: Polling mode
In polling mode, CPU performs MMIO to check if the packet has been copied to the device memory

## Slide 38: Send
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
Firefox puts the packet is at location x in the RAM.
CPU configures (using MMIO) NIC to start a DMA from location x.
CPU puts Firefox to a waiting list and starts executing other threads.

## Slide 39: Send
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
CPU is executing other threads.
NIC is copying packet from memory location x to its internal buffer.
Both things are happening in parallel.

## Slide 40: Polling
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
NIC has copied the packet to its internal buffer. NIC writes something in the memory-mapped area to let the CPU know that copying has been done.

## Slide 41: Polling
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
NIC has copied the packet to its internal buffer. NIC writes something in the memory-mapped area to let the CPU know that copying has been done.
CPU doesn’t know that the packet has been copied. CPU still executing other threads.

## Slide 42: Polling
BIOS ROM
16-BIT DEVICES
VGA DISPLAY
LOW MEMORY
MEMORY MAPPED DEVICES
EXTENDED MEMORY
UNUSED
CPU
The timer interrupt handler is called. CPU reads from memory-mapped area to check if the packet has been copied.
If the answer is yes, CPU sets the packet’s status to sent and puts the Firefox to the ready queue.
TIMER
INTERRUPT

## Slide 43: Polling
Periodically checking for the occurrence of an event
  e.g., after every timer interrupt CPU checks the status of devices
Not good if events are rare
  e.g., keyboard, slow NIC
  Unnecessary wasting CPU in polling
  In these cases, interrupts are useful

## Slide 44: Interrupts
Automatically invoked after a packet is sent/received
If the events are very frequent, the CPU spends most of its time in interrupt handling
  e.g., very fast NIC
  Other applications (not using NIC) will be unnecessary interrupted a lot
  In this case, polling is better

## Slide 45: Example
Firefox invokes receive(buf) system call to receive a packet in the buf
  receive(buf) waits until a packet is received in buf

## Slide 46: receive
#define RX_STATUS_PORT 0x402
#define RX_ADDR_PORT 0x403
struct list *wait_list;
void receive (char *buf) {
/* configure device to copy packet
* to buf when it is received
*/
outl (RX_ADDR_PORT, buf);
outl (RX_STATUS_PORT, 0);
thread_block(wait_list); // put the current thread to wait_list and schedule a new thread
}
Notes: Here the device driver (OS code which communicates with the device) is communicating with the network device to tell the RAM address where an incoming packet needs to be written. The copying may take some time. The driver puts the current thread to a waitlist and schedules a new thread.

## Slide 47: Interrupt
rx_intr is invoked after the device has copied an incoming packet to buf
void rx_intr () {
thread_unblock(wait_list); // remove a thread from wait_list
// and put it to the ready list
}
Notes: The interrupt handler is called when the packet has been written to the buf. It’s time to move the waiting thread to the ready list.

## Slide 48: Polling
rx_poll is invoked after every timer interrupt
#define RX_STATUS_PORT 0x402
void rx_poll() {
if (inl(RX_STATUS_PORT) == 1) // if the device has copied a packet to buf
{
thread_unblock(wait_list); // remove a thread from wait_list
// and put it to the ready list
} }
Notes: In rx_poll, CPU checks if a packet has been copied to buf (using port I/O in this example). If yes, then it puts the waiting thread to the ready list.