## Slide 1: Lecture-1

## Slide 2: Today’s topics
Goals of internet
Network core
Reliability
Design philosophy
Fairness and efficiency
Packet switching
Circuit switching

## Slide 3: Course Webpage
Google classroom: rnj2rhq6

## Slide 4: Books
Computer Networking: A Top-Down Approach, Eighth Edition
  James F. Kurose and Keith W. Ross
Computer Networks: A Systems Approach
  Peterson and Davie

## Slide 5: Tentative plan
Introduction
Internet structure
OSI reference model
Circuit switching vs. Packet switching
Application layer (DNS, SMTP, Socket programming, HTTP)
Transport layer (TCP, UDP, congestion and flow control)
Network layer (IP addressing, ICMP)
Routing algorithms (Link state vs. distance vector, BGP)
Link layer (Ethernet, WiFi, Error detection, ARP, DHCP)
Physical layer

## Slide 6: Grading components
Mid-term: 25
End-term: 45
Assignments (group): 20
Homeworks (group): 10
Maximum group size: 5

## Slide 7: Office hours
Mon, Wed: 12:30 PM – 1:00 PM
Location: A-505, R&D block

## Slide 8: Questions?

## Slide 9: What is the goal of the Internet?
Exchange information between end hosts. These end hosts could be:
  Users connected via laptops, desktops, smartphones, etc.
  Servers hosting websites (e.g., www.chatgpt.com) or streaming services (e.g., Netflix, Prime, etc.)
  Virtual assistants (e.g., Alexa, etc.)

## Slide 10: Communication links
End hosts connect to the Internet using
  Wired (optical fiber, copper cables) network
  Wireless (radio waves, light) network

## Slide 11: Internet protocol
Despite this diversity, all communication across the Internet follows a common protocol called the Internet Protocol (IP)
A protocol is a set of rules or conventions that define how two or more entities exchange information
  Will discuss more about it later

## Slide 12: Connecting end hosts
Direct connection between every pair of hosts?

## Slide 13: Connecting end hosts
Direct connection between every pair of hosts?
  No, that’s impractical. The number of connections would grow rapidly and become unmanageable.

## Slide 14: How is the Internet implemented?
End hosts are connected through a network of gateways such as switches and routers.
Gateways form the backbone of the Internet
Gateways connect to end hosts and other gateways
Forms a large interconnected network

## Slide 15: Connecting end hosts
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 16: Sending a message from A to B
How does internet recognize B?

## Slide 17: Sending a message from A to B
How does internet recognize B?
  Every device has a unique address
A includes B’s address in the message
A sends the message to its nearest gateway
Gateway forward the message toward B

## Slide 18: How gateways forward messages
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 19: How gateways forward messages
Gateways have multiple input/output ports
Use a forwarding table
  The forwarding table maps a destination address to an output port
How forwarding table might have been created?

## Slide 20: How gateways forward messages
Gateways have multiple input/output ports
Use a forwarding table
  The forwarding table maps destination address to output port
How forwarding table might have been created?
  Using shortest path algorithms
Message is forwarded from hop (gateway/end host) to hop until it reaches destination

## Slide 21: How B know who sent it?

## Slide 22: How B know who sent it?
Message includes A’s address
B uses this to identify the sender

## Slide 23: Handling corruption and loss
The message may get corrupted due to electromagnetic interference, signal noise, etc.
It might also get lost due to broken links or power failure
How can we handle corruption and loss?

## Slide 24: Handling corruption and loss
The message may get corrupted due to electromagnetic interference, signal noise, etc.
It might also get lost due to broken links or power failure
Sender sends additional information such as checksum (sum of all characters in the message) with the message
The receiver verifies the checksum and send acknowledgment to sender
If the sender doesn’t receive an acknowledgment, it retransmits the message

## Slide 25: Network core
The network core is the interconnected high-speed gateways and links that forward data between hosts across the internet

## Slide 26: Network core
Internet
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 27: Reliable network core
How can we implement a reliable network core (i.e., the network core handle corruption and loss)?

## Slide 28: Reliable network core
Each gateway sends an acknowledgement to its predecessor
The gateways store a copy of message until an acknowledgement arrives from the next hop
Gateways can also verify the checksum before forwarding the message and discard the message if the checksum doesn’t match
Gateway resends the message if it doesn’t receive an acknowledgment from the next hop

## Slide 29: Reliable network core
Advantage
  Early detection of corruption
  Reduces load on destination host
Problem

## Slide 30: Reliable network core
Advantage
  Early detection of corruption
  Reduces load on destination host
Problem
  A might be sending lot of messages to B. How does the gateway know which message was lost if it doesn’t receive an acknowledgement?
Solution

## Slide 31: Reliable network core
Advantage
  Early detection of corruption
  Reduces load on destination host
Problem
  A might be sending lot of messages to B. How does the gateway know which message was lost if it doesn’t receive an acknowledgement?
Solution
  Only one message is allowed between a pair of hosts
Problem

## Slide 32: Reliable network core
Advantage
  Early detection of corruption
  Reduces load on destination host
Problem
  A might be sending lot of messages to B. How does the gateway know which message was lost if it doesn’t receive an acknowledgement
Solution
  Only one message is allowed between a pair of hosts
Problem
  Too restrictive
Another solution

## Slide 33: Reliable network core
Advantage
  Early detection of corruption
  Reduces load on destination host
Problem
  A might be sending lot of messages to B. How does the gateway know which message was lost if it doesn’t receive an acknowledgement
Solution
  A can add a unique identifier to each message to B
  The gateways can send the unique identifier in the acknowledgement
Problem

## Slide 34: Reliable network core
Advantage
  Early detection of corruption
  Reduces load on destination host
Problem
  A might be sending lot of messages to B. How does the gateway know which message was lost if it doesn’t receive an acknowledgement
Solution
  A can add an unique identifier to each message to B
  The gateways can send the unique identifier in the acknowledgement
Problem
  Additional computational and storage overhead
  Gateways already does a lot of computation to forward messages

## Slide 35: Dealing with corruption
The first approach, in which the end hosts are responsible for reliability, is also called end-to-end check and retry
If failures are rare, it works fine
Used in most cases

## Slide 36: Dealing with corruption
Can the second approach eliminate the retry at the destination host?
or
Can the core network guarantee reliability?

## Slide 37: Dealing with corruption
Can the second approach eliminate the retry at the destination host
or
Can the core network guarantee reliability?
No, the gateways can crash. Other gateways do not have the copies of the lost message.
Solution:

## Slide 38: Dealing with corruption
Can the core network guarantee reliability?
No, the gateways can crash. Other gateways do not have the copies of the lost message.
Solution:
Replicate the same state on multiple gateways. If one fails the other can take over.
Does this guarantee reliability?

## Slide 39: Dealing with corruption
Can the core network guarantee reliability?
No, the gateways can crash. Other gateways do not have the copies of the lost message.
Solution:
Replicate the same state on multiple gateways. If one fails the other can take over.
Does this guarantee reliability?
No, The replication mode can handle a limited number of failures, bounded by the number of replicas.

## Slide 40: Design philosophy of the internet
Gateways are stateless
  They don’t keep track of the intermediate states of an ongoing conversation between two hosts
The state of conversation is maintained at host
  If the host fails, so does the state, also called fate sharing
Fate sharing
  Easy to implement
  Work even if multiple intermediate gateways fail

## Slide 41: Design philosophy of the internet
Reference paper
  The design philosophy of the DARPA internet protocols
    David D. Clark

## Slide 42: Convention
We use the following notational convention for Kb, Mb, and Gb
In networking, units are typically defined using powers of 10, unlike storage systems, which often use powers of 2.
In this course, we will use powers of 10 for both networking and storage.
  Lowercase b means bit
  1 Kb = 1000 bit
  1 Mb = 1000 Kb
  1 Gb = 1000 Mb

## Slide 43: Problem: Fairness
A and B send files to C and D via a common gateway G
A -> 1 Gb file to C
B -> 1 Mb file to D
Rate of transmission of the link: 1 Mbps
If G sees the A’s message first:
C will receive the file after
D will receive the file after

## Slide 44: Problem: Fairness
A and B send files to C and D via a common gateway G
A -> 1 Gb file to C
B -> 1 Mb file to D
Rate of transmission of the link: 1 Mbps
If G sees the A’s message first:
C will receive the file after 1000 seconds
D will receive the file after 1001 seconds

## Slide 45: Problem: Fairness
A and B send files to C and D via a common gateway G
A -> 1 Gb file to C
B -> 1 Mb file to D
Rate of transmission of the link: 1 Mbps
If G sees the A’s message first:
C will receive the file after 1000 seconds
D will receive the file after 1001 seconds
Could D receive the file after 2002 seconds?

## Slide 46: Problem: Fairness
A and B send files to C and D via a common gateway G
A -> 1 Gb file to C
B -> 1 Mb file to D
Rate of transmission of the link: 1 Mbps
If G sees the A’s message first:
C will receive the file after 1000 seconds
D will receive the file after 1001 seconds
Could D receive the file after 2002 seconds?
Yes, if retransmission was done due to corruption or failure.

## Slide 47: Problem: Fairness
Is this scheme fair?

## Slide 48: Problem: Fairness
Is this scheme fair?
  No. Large file blocks the link  other users starve

## Slide 49: Problem: Efficiency
Is this scheme efficient in presence of frequent bit corruption?

## Slide 50: Problem: Efficiency
Is this scheme efficient in presence of frequent bit corruption?
  No, the entire files needs to be retransmitted even if a single bit is corrupted
Solution

## Slide 51: Problem: Efficiency
Is this scheme efficient in presence of frequent bit corruption?
  No, the entire files needs to be retransmitted even if a single bit is corrupted
Solution
  Packetization
    Split the message into small chunks called packets and transmit the packets
    Gateways forward packet in arrival order
    Allows interleaving of packets from different senders

## Slide 52: Packetization

## Slide 53: Packetization
Benefits
  Does it solve the fairness problem?
  Does it solve the efficiency problem?

## Slide 54: Packetization
Benefits
  Improves fairness
  Only corrupted packets need to be retransmitted
  Reduce delay for small transfers
Example:
  A and B send files to C and D via a common gateway G
  A -> 1 Gb file to C
  B -> 1 Mb file to D
  Rate of transmission of the link: 1 Mbps
  Packet size is 1Mb
Is it possible that D receives the file after 4 seconds?

## Slide 55: Packetization
Benefits
  Improves fairness
  Only corrupted packets need to be retransmitted
  Reduce delay for small transfers
Example:
  A and B send files to C and D via a common gateway G
  A -> 1 Gb file to C
  B -> 1 Mb file to D
  Rate of transmission of the link: 1 Mbps
  Packet size is 1Mb
Is it possible that D receives the file after 4 seconds?
  Yes, if B’s packet arrived at G after three packets from A, then D may receive its 1 Mb file after four seconds

## Slide 56: Packet and circuit switching
Read chapter 1.3 from the Kurose and Ross book

## Slide 57: Packet switching
The routers and switches that forward packets are called packet switches (or gateways)
Most packet switches use store-and-forward transmission
  The packet switches must receive the entire packet before forwarding it to the output link
  Queues to temporarily store incoming packets
  Queue size is infinite

## Slide 58: Store and forward
A
B
C
R = 100 Mb/s
R = 1.5 Mb/s
D
E
queue of packets
waiting for transmission over output link
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 59: Packet switching
What will happen if the packets arrive faster than they can be transmitted?

## Slide 60: Packet switching
What will happen if the packets arrive faster than they can be transmitted?
  Packets may accumulate in the queues before they can be processed
  Packets may get dropped if the queue is full
  Packets may experience variable delay

## Slide 61: Circuit switching
In packet switching, packets may experience unexpected delay under heavy load
It could be problematic for real-time applications such as video calls or voice communication
Solution?

## Slide 62: Circuit switching
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 63: Circuit switching
In circuit switching, the network establishes a dedicated end-to-end connection between the two communication hosts A and B
No other hosts can send messages on the dedicated path until A and B decides to end the connection
Does this solves the problem of real-time communication?

## Slide 64: Circuit switching
In circuit switching, the network establishes a dedicated end-to-end connection between the two communication hosts A and B
No other hosts can send messages on the dedicated path until A and B decides to end the connection
Does this solves the problem of real-time communication?
  Yes
Any other problem?

## Slide 65: Circuit switching
In circuit switching, the network establishes a dedicated end-to-end connection between the two communication hosts A and B
No other hosts can send messages on the dedicated path until A and B decides to end the connection
Does this solves the problem of real-time communication?
  Yes
Any other problem?
  Wastage of network resources during the silent period of the communication
    e.g., no one is speaking

## Slide 66: Multiplexing
Even though the circuit switches reserve intermediate links, a link can still serve multiple circuits (dedicated channel between communication hosts) using multiplexing techniques
Time-division multiplexing
  Time is divided into slots
  Each circuit is assigned a slot
  The circuit can use the full transmission rate during its turn in a round-robin manner

## Slide 67: Multiplexing

## Slide 68: Multiplexing
Frequency-division multiplexing (FDM)
  Each communication is assigned a unique frequency band
    e.g., FM radio stations use FDM where each station uses a different frequency in the frequency spectrum
  If the transmission rate is 100 Mbps, then n users sharing the link can roughly send at slightly less than 100/n Mbps