## Slide 2: Today’s topics
Protocol layers
Network security
Socket programming

## Slide 3: References
Peterson and Davie
  Chapter – 1.4
Kurose and Ross
  Chapter 1.5 and 1.6

## Slide 4: Protocol
A formal set of rules that define how two or more entities communicate or interact.
For example: Handshake protocol
  client  server (hello)
  server  client (hello)
  client  server (I received your hello)

## Slide 5: Protocol layers
The Internet follows a layered architecture known as the Internet Protocol Stack
The software and hardware stack for the source and receiver looked like the picture on the right
link
application
network
transport
physical
application
transport
network
link
physical
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 6: Application layer
Includes multiple protocols:
  HTTP (web browsing)
  SMTP (email)
  FTP (file transfer)
  DNS (name resolution: converts website address into its IP address)
The application layer at one end host communicates with the application layer at the other end host.
Packets at this stage are called messages.

## Slide 7: Transport layer
Two main protocols TCP, UDP
TCP provides
  reliable message delivery (handle packet loss, corruption, reordering)
  flow control (a fast sender doesn’t overwhelm a slow receiver)
  congestion control (prevent too much data being injected into the network that can cause packet loss at gateways in the network core)
UDP provides
  connectionless service to applications
    each packet is independent and may arrive out of order or be lost
Packets at this stage are called a segment

## Slide 8: Network layer
Implements the IP protocol
  Adds source and destination IP addresses
Contains routing (packet forwarding) protocols for gateways
Packets here are called datagrams

## Slide 9: Link layer
Used between two directly connected nodes
  i.e., between one hop and the next hop in the path from source to destination
Protocol depends on the link type (Ethernet, Wi-Fi, etc.)
Packets here are called frames

## Slide 10: Physical layer
Transmits bits over the medium (copper, fiber, radio)

## Slide 11: Encapsulation
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
M
Ht
Hn
Hl
M
Ht
Hn
Ht
M
M
M
message
Ht
M
segment
M
Ht
Hn
datagram
frame
M
Ht
Hn
Hl
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 12: Encapsulation
As data moves from the application layer to the physical layer, each layer adds its own header to the packet from the layer above
Intermediate gateways typically process packets only up to the link or network layer.
At the receiver, each layer removes its header and passes data up to the next layer

## Slide 13
network
link
physical
application
transport
network
link
physical
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame
link
physical
End-to-End view
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 14: Link-layer filtering and switching
Wireshark demo

## Slide 15: Link-layer filtering and switching
On a shared channel, such as in a small WiFi network or a group of interconnected computers in an organization, a network interface card (NIC) can receive all the packets transmitted on the medium.
If the NIC had to pass every packet up to the network layer for inspection, it would be very computationally intensive. Instead, the NIC hardware checks the link-layer address (e.g., MAC address) in the link-layer header and only copies packets intended for it into its receive buffer.
Similarly, gateways that forward packets between locally connected devices, such as Ethernet switches, make forwarding decisions using only the link-layer header. They do not need to examine the network-layer (IP) header for normal switching operations.

## Slide 16: Network security

## Slide 17: Network security
Early Network
  The internet was originally designed to trust all the users
  By default, any user can send message to any other user
  The user identity is trusted, rather than being authenticated by default
Today’s network
  Users may not trust each other
    Not even the hardware, software, and communication channel
  Some users may want to remain anonymous
  Mutual trust is an exception

## Slide 18: Malware
While accessing the internet a malicious software known as malware can infect your system
  Malware can delete files, steal your private information such as passwords, infect other devices that are connected to your device, etc.
  Malware can turn your system into a botnet, i.e., a set of compromised devices used to attack other devices.

## Slide 19: Denial of service (DoS) attack

## Slide 20: Denial of service (DoS) attack
Exhaust the server resources by sending too many spurious requests

## Slide 21: Distributed denial of service (DDoS) attack

## Slide 22: Distributed denial of service (DDoS) attack
Multiple sources launch DoS attack on a server

## Slide 23: Packet sniffing
In a shared medium, attackers can capture all passing traffic (e.g., with Wireshark)

## Slide 24: Masquerading

## Slide 25: Masquerading
Sending messages with fake IP addresses to impersonate others

## Slide 26: Defence
You are encouraged to think about the possible defence mechanisms as we progress through this course
We’ll discuss the existing mechanisms as we study the network protocols in more detail

## Slide 27: Application layer

## Slide 28: Applications
The Internet owes its popularity to its killer applications
Think of the web, email, streaming platforms, Internet telephony, and social media — these are what make the Internet a necessity in our daily lives.
Behind the scenes, it’s the application layer protocols that define how two applications talk to each other.

## Slide 29: Application layer
Application layer protocol allows an application on one machine to communicate with an application on another machine connected via the Internet

## Slide 30: Application layer
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
Applications are processes running on a host
Each host on the Internet is identified by a unique IP address
A single host can run multiple applications simultaneously
When a packet arrives at the host, how does it determine which application should receive it?
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 31: Application layer
mobile network
home network
enterprise
network
national or global ISP
local or regional ISP
datacenter
network
content
provider
network
application
transport
network
data link
physical
application
transport
network
data link
physical
application
transport
network
data link
physical
Applications are processes running on a host
Each host on the Internet is identified by a unique IP address
A single host can run multiple applications simultaneously
When a packet arrives at the host, how does it determine which application should receive it?
  A combination of IP address and port number is used to uniquely identify an application
Copyright © 2010-2025 J.F. Kurose, K.W. Ross

## Slide 32: Programming interface
Before diving into the application layer protocols, let’s first talk about the programming interface available to programmers.
All the applications are built using these interfaces.
It will also give you clarity about what services the underlying layers provide to the application layer.

## Slide 33: Linux
On Linux, the OS provides the socket interface
A socket is an endpoint through which a local application connects to the internet
A socket can be created using the socket system call

## Slide 34: socket system call
int socket(int domain, int type, int protocol)
domain:
  PF_INET: Internet family (IPv4)
  PF_UNIX: Unix pipe
  PF_PACKET: direct access to the network driver (bypassing TCP/IP stack)

## Slide 35: socket system call
int socket(int domain, int type, int protocol)
Type:
  SOCK_STREAM: stream socket (TCP)
  SOCK_DGRAM: datagram docket (UDP)
  SOCK_RAW: raw Ethernet frames

## Slide 36: socket system call
int socket(int domain, int type, int protocol)
Protocol:
  IPPROTO_UDP
  IPPROTO_TCP
  IPPROTO_ICMP
  0: if the protocol can be implied from the domain and type

## Slide 37: socket system call
int socket(int domain, int type, int protocol)
Return value:
  A handle (file descriptor) for the newly created socket.
For full details, see "man socket".

## Slide 38: TCP Server
A TCP server typically follows these steps
int bind(int socket, struct sockaddr *address, int addr_len);
int listen(int socket, int backlog);
int accept(int socket, struct sockaddr *address, int *addr_len);

## Slide 39: TCP Server
int bind(int socket, struct sockaddr *address, int addr_len);
  Associates the socket with a specific IP address and port number. The length of an address varies depending on the domain of the socket.
int listen(int socket, int backlog);
  Specifies how many connections can be pending on the specified socket.
int accept(int socket, struct sockaddr *address, int *addr_len);
  Blocks until a client establishes a connection. It returns a new socket descriptor corresponding to the connection established with the client. The client's address is returned via the address parameter.

## Slide 40: TCP Server
This new socket returned by accept is used to exchange data with the client.

## Slide 41: TCP Client
The client also creates a socket using the socket system call.
Then it makes the connect system call.
int connect(int socket, struct sockaddr *address, int addr_len);

## Slide 42: TCP Client
int connect(int socket, struct sockaddr *address, int addr_len);
  During connect, the OS automatically assigns a port number to the client. The client's IP address and port number are passed to the server, which is waiting to accept a connection. If the connection is established, zero is returned.

## Slide 43: Message exchange
Once a connection is established, the application processes invoke the following two system calls to send and receive data:
  int send(int socket, char *message, int msg_len, int flags);
  int recv(int socket, char *buffer, int buf_len, int flags);
Both return the number of bytes successfully sent or received. One error, they return -1.

## Slide 44: UDP
Connectionless protocol
  Listen and accept is not used
recvfrom and sendto for exchanging data
ssize_t sendto(int sockfd, const void *buf, size_t len, int flags, const struct sockaddr *dest_addr, socklen_t addrlen);
ssize_t recvfrom(int sockfd, void *buf, size_t len, int flags, struct sockaddr *src_addr, socklen_t *addrlen);

## Slide 45: UDP message exchange
ssize_t sendto(int sockfd, const void *buf, size_t len, int flags, const struct sockaddr *dest_addr, socklen_t addrlen);
  The application explicitly passes the destination address for each message.
ssize_t recvfrom(int sockfd, void *buf, size_t len, int flags, struct sockaddr *src_addr, socklen_t *addrlen);
  The application receives the sender’s address along with the data.

## Slide 46: UDP vs. TCP
UDP
  Provides a connectionless service.
  No reliability: data packets may get lost.
  Packets may arrive out of order.
  Advantage: suitable for applications tolerant to loss but needing consistent throughput, such as video calls, audio calls, streaming media, and interactive games.
TCP
  Provides a connection-oriented service; communication processes must establish a connection (handshake) before exchanging data.
  Reliable data transfer: no data loss, application receives data in the correct order.
  Applications include file transfer, email, web documents, and smartphone messaging.

## Slide 47: TCP client
void client(char *host) {
char buf[MAX_LINE];
struct sockaddr_in sin;
hp = gethostbyname(host);
if (!hp) {
exit(1);
}
bzero((char *)&sin, sizeof(sin));
sin.sin_family = AF_INET;
bcopy(hp->h_addr, (char *)&sin.sin_addr, hp->h_length);
sin.sin_port = htons(SERVER_PORT);
if ((s = socket(PF_INET, SOCK_STREAM, 0)) < 0) {
perror("simplex-talk: socket");
exit(1);
}
if (connect(s, (struct sockaddr *)&sin, sizeof(sin)) < 0) {
exit(1);
}
while (fgets(buf, sizeof(buf), stdin)) {
send(s, buf, sizeof(buf), 0);
}
}

## Slide 48: TCP server
struct sockaddr_in sin;
char buf[MAX_LINE];
bzero((char *)&sin, sizeof(sin));
sin.sin_family = AF_INET;
sin.sin_addr.s_addr = INADDR_ANY;
sin.sin_port = htons(SERVER_PORT);
if ((s = socket(PF_INET, SOCK_STREAM, 0)) < 0) {
perror("simplex-talk: socket");
exit(1);
}
if ((bind(s, (struct sockaddr *)&sin, sizeof(sin))) < 0) {
exit(1);
}
listen(s, MAX_PENDING);
if ((new_s = accept(s, (struct sockaddr *)&sin, &addr_len)) < 0) {
exit(1);
}
// recv blocks until some data is available on the socket
buf_len = recv(new_s, buf, sizeof(buf), 0);
fputs(buf, stdout);
close(new_s);